## Slide 1: Transistors and Biasing Methods
Unit-2

## Slide 2: Contents:
Transistors:
Bipolar Junction Transistor
Transistor Voltages and Currents
Amplification
Common Base Characteristics
Common Emitter Characteristics
Common Collector Characteristics
DC Load Line and Bias Point

## Slide 3: Contents:
Biasing Methods:
Base Bias
Collector to Base Bias
Voltage Divider Bias
Comparison of basic Bias Circuits

## Slide 4
1. Bipolar junction Transistor (BJT)

## Slide 5
A bipolar transistor is a semiconductor device in which electric current flows due to electrons and holes BOTH, simultaneously. Thus both types of charges take part in the conduction of current through it. Hence it is called bipolar transistor.
A bipolar junction transistor (BJT) consists of two PN junctions formed by sandwiching either p-type or n-type semiconductor between a pair of opposite types.
Bipolar junction Transistor

## Slide 6: Bipolar junction Transistor
These are two types 1. NPN 2. PNP transistor
The outer layers of the npn or pnp sandwich are called the emitter and the collector, and the centre layer is termed the base.
Two pn junctions are formed with depletion regions and barrier voltages at each junction.

## Slide 7: Bipolar junction Transistor (or) Operation of PNP or NPN
A transistor (PNP or NPN) has three sections of doped semiconductors.
It consists of 3 terminals
1.Emitter 2. Base 3. Collector
Section on one side that supplies charge carriers (electrons of holes) is called emitter. Which is heavily doped .
The middle section which form two pn-junctions between the emitter and collector is called the base.

## Slide 8: Bipolar junction Transistor
The section on the other side that collects the charges is called the collector . Collector junction is always reverse biased. This section is moderately doped.
Where as emitter is heavily doped so that it can inject a large number of charge carriers into the base.
The base is lightly doped and very thin.
The resistance of emitter diode is small and collector diode is large.
Therefore the transistor transfers the input signal current from a low-resistance circuit to a high-resistance circuit.

## Slide 9
The base section is made as narrow as possible so that charge carriers can easily move across from emitter to collector.
The base is lightly doped, so that few charge carriers are available to recombine with the majority charge carriers from the emitter.
Most charge carriers from the emitter flow to the collector, a few flow out through the base terminal.

## Slide 10: Operation of NPN and PNP

## Slide 11: Transistor operating regions.

## Slide 12
A transistor can be operated in three different regions as
a) Active region b) Saturation region c) Cut-off region
Active region: The transistor is said to be operated in active region when the emitter-base junction is forward biased and collector –base junction is reverse biased.
The collector current is said to have two current components one is due to the forward biasing of EB junction and the other is due to reverse biasing of CB junction.
The collector current component due to the reverse biasing of the collector junction is called reverse saturation current (ICO or ICBO) and it is very small in magnitude.

## Slide 13
Saturation Region:
Transistor is said to be operated in saturation region when both EB junction and CB junction are forward biased as shown. When transistor is operated in saturation region IC increases rapidly for a very small change in VC.
Cut-off region:
When both EB junction and CB junction are reverse biased, the transistor is said to be operated in cut-off region. In this region, the current in the transistor is very small and thus when a transistor in this region it is assumed to be in off state.

## Slide 14: 2. Transistor Voltages and Currents

## Slide 15: 3. Amplification
A transistor raises the strength of a weak signal and thus acts as an amplifier.
The weak signal is applied between emitter-base junction and output is taken across the load Rc connected in the collector circuit.
The input circuit should always remain forward biased. To do so, a dc voltage VEE is applied in the input circuit in addition to the signal.

## Slide 16: Amplification
This dc voltage is known as bias voltage and its magnitude is such that it always keeps the input circuit forward biased regardless of the polarity of the signal.
As the input circuit has low resistance, therefore, a small change in signal voltage causes and appreciable change in IE. This causes almost the same change in IC due to transistor action. The collector current flowing through a high load resistance RC produces a large voltage across it. Thus a weak signal applied in the input circuit appears in the amplified form in the collector circuit.
In this way the transistor acts as an amplifier.

## Slide 17
4. COMMON BASE CHARACTERISTICS

## Slide 18: Common base characteristics
A pnp transistor with its base terminal common to both the input (emitter-base) terminal and the output (collector-base) terminal.
The transistor is said to be connected in common-base configuration.
Voltmeters and ammeters are used to measure the input and output voltages and currents.

## Slide 20: Common-Base Input characteristics
To investigate the input characteristics, the output voltage (VCB) is kept constant, and the input voltage (VEB) is set at several convenient levels.
At each input voltage, the corresponding input current (IE) is recorded.
The IE and VEB levels are then plotted to give the common-base input Characteristics.

## Slide 21: Input Characteristics

## Slide 22: Common base Output characteristics
To investigate output characteristics, the input current (IE) is kept constant, and VCB is adjusted in convenient steps, and the corresponding values of IC are recorded.
The corresponding IC and VCB levels obtained when IE was held constant at 1 m A are potted, and the resultant characteristic is identified as IE =1mA. Similarly other characteristics are potted for IE equal to 2mA, 3mA, and so on

## Slide 23: Output Characteristics

## Slide 24
5. COMMON EMITTER CHARACTERISTICS

## Slide 25: COMMON-EMITTER CHARACTERISTCS
A pnp transistor with its Emitter terminal common to both the input (base-emitter) terminal and the output (collector-emitter) terminal.
The transistor is said to be connected in common-emitter configuration.
Voltmeters and ammeters are used to measure the input and output voltages and currents.

## Slide 27: Common-Emitter Input Characteristics
To investigate the input characteristics, the output voltage (VCE) is kept constant, and the input voltage (VBE) is set at several convenient levels.
At each input voltage, the corresponding input current (IB) is recorded.
The IB and VBE levels are then plotted to give the common-emitter input Characteristics.

## Slide 29: Common Emitter output characteristics
To investigate output characteristics, the input current (IB) is kept constant, and VCE is adjusted in convenient steps, and the corresponding values of IC are recorded.
The corresponding IC and VCE levels obtained when IB was held constant at 10 µ A are potted, and the resultant characteristic is identified as IB=10 µ A. Similarly other characteristics are potted for IB equal to 20 µ A, 30 µ A, and so on.

## Slide 31
6. COMMON COLLECTOR CHARACTERISTICS

## Slide 32
In this circuit the base terminal of the transistor serves as the input, the emitter is the output, and the collector is common to both.
Signal input between base and common collector.
Signal output between emitter and common collector.
The CC circuit is also known as an emitter follower since the output voltage at the emitter follows the input voltage at the base.
It has voltage gain slightly less than unity.
COMMON COLLECTOR CHARACTERISTICS

## Slide 34
Common Collector Input Characteristics
The CC input characteristics are quite different from CB & CE characteristics.
This is because input voltage VBC is largely determined by output voltage VEC
VEB =V EC - VBC
As VBC increases with VEC constant VEB decreases hence IB decreases.

## Slide 35
Common Collector Output Characteristics
Here VCE increases IE also increases.
Just as in common emitter output characteristics IC increases with increasing IB ,so IE also increases here with increasing IB.
Hence for constant VEC, IE increases with IB

## Slide 36
α is common base current gain
α dc = IC / IE
β is common emitter current gain
β = IC / IB
IC = α dc ( IC + IB)
IC = α dc IB / 1- α dc
IC = β dc IB
β = α dc / 1- α dc

## Slide 37: Early Effect
An increase in magnitude of collector voltage increases (reverse bias) the space charge width increase at the output junction diode (C-B junction). Such action causes the effective base width ‘W’ to decreases. This phenomenon is known as ‘Early Effect’

## Slide 38: Punch-through (or) Reach -through
If an excessive reverse-bias voltage is applied to the collector-base junction, the device breakdown may occur.
Breakdown can also result from the collector-base depletion region penetrating into the base (as the reverse bias increases) until it makes contact with emitter-base depletion region.
This condition is known as punch through or reach through
A Very large currents can flow when it occurs, possible destroying the device.

## Slide 40: Thermal run away

## Slide 41: Thermal run away
The Junction temperature may rise either because of the ambient temperature or because of self heating.
As the junction temperature increases, Ico increases which will further increase Ic . Again heat dissipates causing the temperature to increase.
It is a cumulative process Which will cause the transistor to burn out.

## Slide 42: Transistor as a switching
Transistor can be used as a switch
For obtaining switching characteristics saturation and cutoff regions are taken into consideration.
Saturation region is known as on condition of a switch.
cutoff region is known as off condition of a switch.

## Slide 44: Transistor Switching timings

## Slide 46: Transistor switching timings
Current does not Respond to input signal. There exists certain time delay.
Delay time td
The delay time that elapses with the time required for the current to rise 10 % of maximum value is called delay time.
Rise time tr
IT is the time required for the current to rise from 10 % of its maximum value to 90 % of its maximum value.

## Slide 47: Transistor switching timings
Storage time ts :
The interval Which elapses the transition of input wave form and The time when IC has dropped to 90% of maximum value is called storage time ts .
Fall time tf :
The time required to fall from 90% of its maximum value to 10% of maximum value is known as fall time tf .

## Slide 48: Transistor switching timings:
Transistor switching timings are
Delay time (td)
Rise time (tr)
Turn on time (ton) : (ton) = (td)+ (tr)
It is the sum of delay time and rise time.
Turn off time (t off): (toff)= (ts)+ (tf)
Storage time (ts)
Fall time (tf)
Turn off time is the combination storage time and fall time

## Slide 49: Transistor Biasing
The basic function of transistor is amplification. The process of raising the strength of weak signal without any change in its general shape is referred as faithful amplification. For faithful amplification it is essential that:-
Emitter-Base junction is forward biased
Collector- Base junction is reversed biased
Proper zero signal collector current
The proper flow of zero signal collector current and the maintenance of proper collector emitter voltage during the passage of signal is called transistor biasing.

## Slide 50
WHY BIASING?
If the transistor is not biased properly, it would work inefficiently and produce distortion in output signal.
HOW A TRANSISTOR CAN BE BIASED?
A transistor is biased either with the help of battery or associating a circuit with the transistor. The later method is more efficient and is frequently used. The circuit used for transistor biasing is called the biasing circuit.

## Slide 51
BIAS STABILITY
Through proper biasing, a desired quiescent operating point of the transistor amplifier in the active region (linear region) of the characteristics is obtained. It is desired that once selected the operating point should remain stable. The maintenance of operating point stable is called Stabilization.
The operating point of a transistor amplifier shifts mainly with changes in temperature, since the transistor parameters — β, ICO and VBE are functions of temperature.

## Slide 53: 7. A generic dc load line.

## Slide 54: Example
Plot the dc load line for the circuit shown in Fig

## Slide 55: Example
Plot the dc load line for the circuit shown in Fig. Then, find the values of VCE for IC = 1, 2, 5 mA respectively.
IC (mA) | VCE (V)
1 | 9
2 | 8
5 | 5

## Slide 56
The DC Operating Point
For a transistor circuit to amplify it must be properly biased with dc voltages. The dc operating point between saturation and cutoff is called the Q-point. The goal is to set the Q-point such that that it does not go into saturation or cutoff when an a ac signal is applied.

## Slide 57: 1. Base bias (fixed bias).
b = dc current gain = hFE

## Slide 58: Example
The circuit is midpoint biased.

## Slide 59: Example
Construct the dc load line for the circuit shown in Fig and plot the Q-point from the values obtained in Example .Determine whether the circuit is midpoint biased.

## Slide 60: Base bias characteristics.
Advantage: Circuit simplicity.
Disadvantage: Q-point shift with temp.
Applications: Switching circuits only.
Circuit recognition: A single resistor (RB) between the base terminal and VCC. No emitter resistor.

## Slide 61: Base bias characteristics.
Load line equations:
Q-point equations:

## Slide 63: 2. Collector-feedback bias.

## Slide 64: Example
Determine the values of ICQ and VCEQ for the amplifier shown in Fig.

## Slide 65: Circuit Stability of Collector-Feedback Bias
hFE increases
IC increases (if IB is the same)
VCE decreases
IB decreases
IC does not increase that much.
Good Stability. Less dependent on hFE and temperature.

## Slide 66: Collector-Feedback Characteristics
Q-point relationships:

## Slide 67: Collector-Feedback Characteristics
Circuit recognition: The base resistor is connected between the base and the collector terminals of the transistor.
Advantage: A simple circuit with relatively stable Q-point.
Disadvantage: Relatively poor ac characteristics.
Applications: Used primarily to bias linear amplifiers.

## Slide 68: Thermal stability factor of collector feedback bias

## Slide 69
Applying KVL through base circuit
we can write (Ib+ IC) RC + Ib Rb+ Vbe= Vcc
Diff. w. r. t. IC we get
(∂Ib / ∂Ic) = - RC / (Rb + RC)
Therefore, SIco ═ (1+ β)
1+ [βRC/(RC+ Rb)]
Which is less than (1+β), signifying better thermal stability

## Slide 70: 3. Voltage divider bias
Assume that I2 > 10IB.
Assume that ICQ @ IE (or hFE >> 1). Then

## Slide 71: Example
Determine the values of ICQ and VCEQ for the circuit shown in Fig.
Because ICQ @ IE (or hFE >> 1),

## Slide 72: Example
Verify that I2 > 10 IB.

## Slide 73: Stability of Voltage Divider Bias Circuit
The Q-point of voltage divider bias circuit is less dependent on hFE than that of the base bias (fixed bias).
For example, if IE is exactly 10 mA, the range of hFE is 100 to 300. Then
ICQ hardly changes over the entire range of hFE.

## Slide 74: Voltage-divider bias characteristics
Circuit recognition: The voltage divider in the base circuit.
Advantages: The circuit Q-point values are stable against changes in hFE.
Disadvantages: Requires more components than most other biasing circuits.
Applications: Used primarily to bias linear amplifier.

## Slide 75: Voltage-divider bias characteristics
Load line equations:
Q-point equations (assume that hFERE > 10R2):

## Slide 76: Thermal stability factor of voltage divider bias

## Slide 78: 4.Comparison of Bias Circuits
Parameter | Fixed Bias | Feedback Bias | Self Bias
Stability | 1+β | <1+β | 1
Complexity | Simple (requires only RB) | Simple (requires only RB) | Requires R1 ,R2 and RE .
Usage | Switching Circuits | Used in circuits which should not drive transistor into saturation | Universal bias circuit. (always preferred)
Stability factor | S=1+β | S=1+β / 1+β(RC/RC+RB) | S=1+β / 1+β(RE/RE+RT)

## Slide 79
The End